Digital electronics recap
prepared for Programmable Logic Lessons / 1.1 by ~skmp
Kindly hosted by hackerspace.gr

---
Binary system
Simplest counting system
Only two symbols:
0, 1
(Also known as
False, True
bit)

---
Bool algebra
- Logic using the binary system
- Basic operations
  - And
    - If x and y. Common symbols &, &&, *
  - Or
    - X or Y. Common symbols |, ||, + (in bool algebra)
  - Xor
    - X or Y, but not X and Y. Common symbols: ^ (C/C++), ⊕
  - Not
    - Inverse. Common symbols: ~, -

---
Truth tables
(An easy easy to remember)
x	y	X and Y	X Or y	X Xor y	Not X
0	0	0	0	0	1
0	1	0	1	1	1
1	0	0	1	1	0
1	1	1	1	0	0

---
Doing useful work !
- Numbers with many digits
  - 0110101
    - Each digit represents an increasing power of 2 (RtL)
      - 1 * 2^0 + 0 * 2^1 + 1 * 2^2 + 0 * 2^3 + 1 * 2^4+ 1 * 2^5+0 * 2^6
      - 1*1 + 0*2 + 1*4 + 0*8 + 1*16 + 1*32 + 0*64
      - = 53 (base 10)
  - base 16 (Hex) is also handy for large numbers
    - 0-9, A, B, C, D, E, F
    - 0xF0E3
      - 3*16^0 + E*16^1 + 0*16^2+ F*16^3
      - 3 + 14*16 + 0*256 + 15*4096
      - = 61667 (base 10)
    - Base 16 ↔ 2 conversions are easy (Google it up)

---
Doing useful work !
- Representing Negative numbers
  - 2's complement
    - -x is defined as ~x + 1
    - For 8 bits, -128 to 127
    - -01010 → 10110
  - 1's complement (not used anymore)
    - -x is defined as ~x
  - Sign bit
    - An extra bit to store positive or negative
    - For 8 bits, -127 to 127, with +0 and -0
      - 7 bits range and sign bit

---
Doing useful work !
- Bit-wise operators
  - And, Or, Xor, Not
    - Each bit is processed in “parallel”
      - z = x and y → z[0] = x[0] and y[0], z[1] = x[1] and y[1], and so on
- Math primitives
  - Addition, Subtraction, Multiplication (sometimes)
    - http://en.wikipedia.org/wiki/Adder_(electronics)
    - http://en.wikipedia.org/wiki/Binary_multiplier
- Memory & Routing
  - Flip flop (Memory)
    - http://en.wikipedia.org/wiki/Flip-flop_(electronics)
  - Mux/Demux (Selection/Routing)
    - http://en.wikipedia.org/wiki/Multiplexer

---
Flip flops
- memory elements
  - S/R (Set/Reset)
    - Basic building block
  - Other Types
    - J/K is like S/R, but clocked
    - D (Data)
    - T (Toggle)

---
Mux/Demux
- Use an input signal to select from two (or more) inputs
  - Basic logic that allows if/conditions/selection
- Demux is the inverse operation

---
Combinational logic
- Output only depends on input
  - Typical example is an Adder
- Summarized in truth tables
  - http://en.wikipedia.org/wiki/Truth_table
- http://en.wikipedia.org/wiki/Combinational_logic

---
Sequential Logic
- Output depends on past values
  - The system has “memory”
  - Typical example is a counter
    - The output depends on the internal state
- Is usually synchronized via a global clock
- Typically summarized in Transition/Excitation Tables
  - http://en.wikipedia.org/wiki/State_transition_table
  - http://en.wikipedia.org/wiki/Excitation_table
- http://en.wikipedia.org/wiki/Sequential_logic

---
Other useful links
(for wikipedia addicts)
- http://en.wikipedia.org/wiki/Theory_of_computation
  - http://en.wikipedia.org/wiki/Automata_theory
  - http://en.wikipedia.org/wiki/Finite_state_machine
- http://en.wikipedia.org/wiki/Asynchronous_circuit
- http://en.wikipedia.org/wiki/Synchronous_system
- … :)

---
Thanks !
Next week we'll do some hands-on “experiments” on an actual fpga !
Feel free to drop by #hsgr @ freenode
... or the hsgr mailing list
... and use the wiki !
(or, send direct feedback – skmp@emudev.org)